## Slide 1
csWeb
GUI
FloodSim
Service
Load and replay flooding simulations
ElectrSim
Service
Simulate effects of power failures
Cure & Care
Service
Simulate effects of power failures
CommSim
Service
Simulate effects of power/flooding on comm.
CritObjSim
Service
Simulate effects of power/flooding on critical obj.
RoadSim
Service
Simulate effects of power/flooding on roads
Publish / Subscribe bus (existing implementations in MQTT and IMB)
csWeb
Web GUI
WebSockets (Socket.io)
SimService
Manager
Time mgmt, heartbeat,
scenario prep, start/stop
SimService
Web GUI
csWeb
GUI
csWeb
Desktop GUI
csWeb
Manager
REST
Notes: The csWeb manager is running on node.js: it has several connectors for receiving information, such as MQTT (Message Queue), IMB (proprietary binary TNO protocol), REST, MongoDB and file storage. It communicates with the GUIs through WebSockets: when a user sets a feature’s property, like the water level a hospital can withstand, it will communicate it to all other connected GUIs, as well as the simulation backend. Similarly, when one of the simulations updates the state of an object (e.g. moving from OK to Failed, it will update all GUIs that are displaying this feature too.
The SimService manager derives from the csWeb manager, and adds simulation and time management functionality as well as state management (it incorporates a Finite State Machine with states like running, paused, etc.).
Each of the specific simulations derive from the SimService manager, so they are also time-aware, have a heartbeat, and a state. They listen to the MQTT channel to receive updates, e.g. a flooding or blackout message, or messages from the GUI that set certain properties like the UPS backup power duration. Typically, they communicate GeoJSON objects, either complete GeoJSON map layers or specific GeoJSON features (like a hospital).
In order to create a new simulation scenario, all that is required are the initial map layers as well as any flooding simulations that you wish to run (note that you can also decide to start with another incident, e.g. a power failure). Map layers are in the GeoJSON format, where each feature on the map is represented with its coordinates and a list of properties (e.g. water resistance, UPS, number of beds, etc.). For the flooding simulation, we use another geo standard, i.e. the ESRI ASCII grid format, where each grid has to use the WGS84 coordinate reference system, each cell contains the water height in meters above the ground, and the name of the file is a number representing the number of minutes since the start of the simulation. At the beginning of the scenario, the initial data is loaded, and is updated during the simulation, so each run can start afresh.